Wave packets in a thin Timoshenko-like shell with variable parameters

Pavel Aleksandrovich Gladkov

Post-graduate student, Vitebsk State University

Non-stationary waves propagating in an axially symmetric non-homogeneous thin Timoshenko-like shell with variable thickness, density, Young’s modulus and Poisson’s ratio are studied. A formal asymptotic solution of the equations governing the wave process is constructed in the form of short localized waves named as the wave packets (the WP) and running along the longitudinal axis of the shell. The solution represents a superposition of bend and longitudinal waves.

All variable functions are expended into the series in a neighborhood of the moving center  called the wave packet center. The solution of a Timoshenko-like set of differential equations is constructed in a form

,

,

where , ,  is a dimensionless longitudinal co-ordinate.

A small parameter ( is introduced for studying the packets of short waves propagating in the longitudinal direction, with the momentary frequency  and the wave length being of the order (. The functions  are polynomials in ,  is the wave number, the function  characterizes the width of the WP in the longitudinal direction,  for any t.  It is important to note that the last inequality guarantees the attenuation of the wave amplitudes within the packet.

The zeroth order approximation problem has a solution if and only if the condition

holds. Here

is the Hamiltonian function with  a modulus of subgrade reaction, E and  Young’s modulus and Poisson’s ratio and  is a density. The signs  indicating the availability of two branches (positive and negative) of the solution. Then the solution of zeroth order approximation problem may be presented as , where  is an unknown polynomial in (.

The compatibility condition for the non-homogeneous problem arising in the first order approximation gives the Hamiltonian system

.

The condition for the existence of a solution of the non-homogeneous problem in the second order approximation produces the Riccati equation

and the amplitude equation

,

where the  are known functions.

In particular, if the Young’s modulus is variable, then the constructed solution permits to investigate high-frequency free oscillations of the medium in a neighborhood of the so-called “weakest” plane where function  is maximum. The qualitative analysis of the Hamiltonian system has also allowed to reveal that the presence of the “weakest” plane may result in strong localization of the non-stationary wave processes near this plane and also in the effects of the reflection of the running wave packets, these reflections being accompanied by strong focusing and growing amplitudes in the packets.